## Slide 1: Slap Back Echo
Tor Halmrast Head of Acoustics, Statsbygg Assoc. Prof., Univ. Oslo, Musicology
2017
Art of Record Production, St.holm 1-3 dec 2017

## Slide 2
Jeg har aldri vært Elvis-fan
Vanligvis: Tape/elektronikk etterlikne naturlige fenomener
Artikkel om Elvis´s plateinnspillinger:
Hvordan man «naturlig» prøvde å etterlikne noe som først ble lagd «på tape»
SUN STUDIOS, Memphis
RCA, Nashville og Hollywood

## Slide 3
Interesse:
Klangfarge-endringer pga nære refleksjoner
Et ekko er ikke et ekko
Direktivitet av ekko
Signalbehandling: Cepstrum, Autocorrelation etc.

## Slide 4
Sam Phillips The Memphis Recording Service. SUN Studios
60 -120 milliseconds?
At 60 Milliseconds, you don’t hear much doubling, but everything sounds a little thicker and fatter At 120 Milliseconds you are REALLY starting to hear the distinct doubling of the sound.
530ms will be too long, 163 ms seemed to sound about right. …a little either side of a 1/16 note might be what it really comes down to.
(75 to 250 milliseconds), with little or no feedback.
re-feeding the output signal from the playback head tape recorder to its record head
The physical space between heads, the speed of the tape, and the chosen volume being the main controlling factors.
150 to 200ms with just one repeat at almost the same amplitude as the original signal.
Scotty Moore’s guitar-work on “That’s All Right”
2 Ampex 350 recorders:

## Slide 5: SUN Studios, Memphis
Jerry Lee Lewis, Carl Perkins Elvis Presly Johnny Cash SUN STUDIOS Dec.4th, 1956
Sam Philips
ELVIS
2017

## Slide 6
Perforated gypsym (mid-freq.-absorber)
- Bass abs.!!
Sun Studios
T30 (from short vocal sound)

## Slide 7
“Baby Let´s Play House”.
Acoustical Energy Decay, 1/1 oct. 250 Hz from short voice uttering followed by “almost silence” .

## Slide 8
Baby Let´s Play House
137 ms
Power Cepstrum (Praat):
Sun Studios

## Slide 9
Tryin´to get to you
137 ms
Power Cepstrum (Praat)
Cepstrum (MIR toolbox)
Autocorrelation (MIR toolbox)
PITCH (by Autocrrelation)
137 ms
Sun Studios

## Slide 11
Tomorrow Night
Cepstrum
Autocorrelation
150 ms
Overdubbing??

## Slide 12
RCA

## Slide 13
January 1956 : Heartbreak Hotel was recorded - perhaps they found out the hard way when they had to use the stairwell.
Elvis moved to the bigger RCA company They did not figure out
how Sam Philips had made the Slap Back Echo

## Slide 15
Heartbreak Hotel
82 msec
RCA
Tone E=330

## Slide 16
deltaT=0,08 s (80 ms) CBTB=1/deltaT=1000/80=12.5 Hz
RCA
MIGHT correspond to an echo in the length direction of a corridor with length 27.2/2=13.6 m (if the sound travels to the «short wall» and back)

## Slide 17
Heartbreak Hotel (cont.)
1500 Hz
75 Hz
22.000 Hz
80 Hz
RCA

## Slide 18
Heartbreak Hotel (forts.)
Spectrum of first part (Since my …), mostly a (somewhat low) E
No clear comb-filter(?)

## Slide 19
Heartbreak Hotel (cont.)
(wEEEL, sIIIIInce )
Formant1/Formant2 (from litt.) e: 402 / 2020, i: 291/2210
FORMANTS

## Slide 20
"cepstrum" =reversing the first four letters of "spectrum".
ceptrum = the inverse Fourier transform of the log magnitude spectrum.
complex cepstrum, real cepstrum, power cepstrum, phase cepstrum

## Slide 21
vocal excitation (pitch) and vocal tract (formants) are
additive in the logarithm of the power spectrum and
thus clearly separate.
convolution of two signals = addition of their complex cepstra:
The cepstrum projects all the slowly varying components in log magnitude spectrum to the low frequency region and fast varying components to the high frequency regions.
In the log magnitude spectrum, the slowly varying components represent the envolope corresponds to the vocal tract and the fast varying components to the excitation source.
As a result the vocal tract and excitation source components get represented naturally in the spectrum of speech. The initial few values in the cepstrum typically 13-15 cepstral values represent the vocal tract information

## Slide 22
SIFT Simplified Inverse Filter Tracking algorithm
Encompasses the desirable properties of both autocorrelation and cepstral pitch analysis techniques.
The complex cepstrum is defined as the Inverse Fourier transform of the logarithm (with unwrapped phase) of the Fourier transform of the signal. This is sometimes called the spectrum of a spectrum.
complex cepstrum of signal = IFT(log(FT(the signal))+j2πm) (where m is the integer required to properly unwrap the angle or imaginary part of the complex log function)
Many texts define the process as FT → abs() → log → IFT, i.e., that the cepstrum is the "inverse Fourier transform of the log-magnitude Fourier spectrum". (the difference between squaring or taking the absolute value amounts to an overall factor of 2)
The power cepstrum =squared magnitude of the inverse Fourier transform of the logarithm of the squared magnitude of the Fourier transform of a signal

## Slide 23
Sound File
Autocorrelation
Cepstrum
HUMAN ORAL CLICK w/REFLECTION 10ms FREQUENCY SPECTRUM:
The signal «looks like itself» after 0 ms (of course) and after 10 ms
The frequency response (spectrum) «looks like itself» every 100 Hz (which corresponds to 1/100=0.001 seconds=10 milliseconds

## Slide 24
SPECTRUM CBTB= 1/Δt CBTB=1000/137=7,3 Hz (1029.3-1022)
Dirac + reflection
Δt =137 ms
POWER CEPSTRUM
As for
SUN studios

## Slide 25
COMB FILTERS
CBTB=CombBetweenTeethBandwidth =
PS! For 50 ms: CBTB=1000/50=20 Hz
DELAY: SHORT MEDIUM LONG
=10 ms

## Slide 26
ECHO-------------------------------------------------------------------------
Fund. Voice
For- mants.
Room reso- nances
Flut- ter 2kHz tail
Box Klang- Farbe
POWER CEPSTRUM

## Slide 27
ECHO--------
Fund. Voice
For- mants.
Room reso- nances
Flut- ter 2kHz tail
Box Klang- Farbe
POWER CEPSTRUM

## Slide 28
PERCEIVED COMB FILTER COLORATION? (BOX-KLANGFARBE) Comparing the CBTB (Comb Between Teeth Bandwidth) with the Critical Bandwidth of our hearing organ (basilar membran)

## Slide 29
SUN SlapBack No CombColoration
Heartbreak VeryLittleColoration
LongTallSally CorridorColoration?

## Slide 30
Slap Back Echo Happily in MONO
Heartbreak Hotel Orig (Hallway-reverb, no real Slap Back)
Added Slap Back Echo 137 ms MONO
Orig. LEFT, Slap Back Echo: RIGHT
Orig. CENTER Slap Back Echo: RIGHT

## Slide 31
Separate Voice and Reflection?
LPC= LINEAR PREDICTIVE CODING
PS! Did not work for detecting echoes, beacuse this LPC algorithm smoothes also the attacks, so the delayed echo is not detectable, but «funny»!!
Orig. Heartbreak Hotel LPC w/WhiteNoise
LPC Residue (= Voice/pitch)

## Slide 32
Long Tall Sally
RCA

## Slide 34
1.82 m

## Slide 35
9.7 ms: a reflection?
Short delay time ≈ voice
Fundamental pitch in this short clip of Long Tall Sally ≈ 330 Hz,
Δt= 1/330=3 ms.
Power Cepstrogram of “Long Tall Sally”.
Quefrequencies corresponding to the fundamental
pitch indicated as the lowest number to the right
We do not see an additional, strong spike at 9.7 ms
A first indication that there is no strong, distinct floor reflection
with a delay of 9.7 ms. (also because 9.7 is close to 3x3=9 from the voice).
Eliminate the fundamental and overtones of the voice,
a Linear Predictive Coding (LPC); exchanging Elvis´ voice chords with white noise as excitation.
The result sounds like Elvis whispering “Gon´na Tell Aunt Mary”.
Power Cepstrum of this sound file (unfortunately)
gave no clear indication of a strong, distinct reflection after
9.7 ms.
Autocorrelation of this is sound file shown in figure App.2.
We might see that there is a somewhat higher value for app. 9.7 ms,
but this is not very strong and also “smeared out” in time,
so if this was a floor reflection, the singer must have moved his head somewhat
during the recording, so that the distance from the floor changed over time,
a highly reasonable assumption for Elvis.
“wah-wah-pedal-effect”?.
Autocorrelation of Linear Predictive Coding of “Long Tall Sally” with white noise as excitation.

## Slide 36
CONCLUSION SLAP BACK ECHOS, SUN STUDIOS (Baby Let´s Play House, Tryin´to get to you) single tape echo:
TIME DOMAIN and not much comb-filter coloration MONO!!!!!!!!!
RCA recordings (Heartbreak, Long Tall Sally) Shorter Delay, Not so Distinct., MIGHT correspond to an echo in the length direction of a corridor with length 27.2/2=13.6 m (if the sound travels to the «short wall» and back) Tendencies of shorter repetitions (repetetive reflections each 9 ms), that might PERHAPS be flutter-echo between side walls in a corridor with a width of app.3 m
Small tendency og Box-Klangfarbe and the possible 9ms probably adds to the CloseRoom sound perceived as «intimacy»
137 ms
82 ms